BEFORE

the National Aeronautics and Space Administration

Federal Register Docket No. 2010-21052, Notice 10-093

National Environmental Policy Act;

NASA Glenn Research Center Plum Brook Station

Wind Farm Project

COMMENTS

Submitted ON BEHALF OF the STAFF OF

THE OHIO POWER SITING BOARD

On Proposed Environmental Impact Statement

Scoping for the NASA Glenn Research Center

October 22, 2010

COMMENTS

Submitted ON BEHALF OF THE STAFF OF

THE OHIO POWER SITING BOARD

On Proposed Environmental Impact Statement

Scoping for the NASA Glenn Research Center

In Ohio, the Ohio Power Siting Board (OPSB) has regulatory jurisdiction for approving the construction of “major utility facilities”.  A “major utility facility”, as defined by Section 4906.01, Ohio Revised Code, includes “electric generating plant and associated facilities designed for, or capable of, operation at a capacity of fifty megawatts or more.”  In addition, the OPSB has jurisdiction over “economically significant wind farms,” defined as follows:

. . . wind turbines and associated facilities with a single interconnection to the electrical grid and designed for, or capable of, operation at an aggregate capacity of five or more megawatts but less than fifty megawatts.

It is with this background that the OPSB Staff submits comments pertaining to the EIS scoping efforts for the NASA Glenn Research Center Plum Brook Station Wind Farm, noticed in the Federal Register on August 25, 2010 (p. 52374 – 52375).

According to the Supplementary Information in the Federal Register, the potential wind farm project would consist of 20 to 30 wind turbines, with a rated capacity of 2.5 megawatts (MW) each, and a total maximum project capacity of 70 MW.

The Federal Register directs that, “[w]ritten comments, statements, and or questions regarding the alternatives or environmental impacts should identify issues or suggest topics to be included in this EIS.”  The Staff of the OPSB offers the following comments consistent with that direction.

For the proposed wind turbines, electric collection system, access roads, and other facilities associated with the potential Plum Brook Station Wind Farm, OPSB Staff recommends that the EIS consider, at minimum, the following factors:

- Temporary and permanent impacts to surface waters (i.e., wetlands, streams, etc)

- Direct and indirect impacts to wildlife

- Potential impacts to cultural resources, including both archaeological and architectural resources

- Site geology

- Noise – during both construction and operation

- Visual impact (i.e., aesthetics)

- Shadow flicker

- Communication interference

- Radar interference

- Ice throw

- Blade shear

- Decommissioning

- Impacts to regional electric power grid

- Impacts to roads and bridges from construction/equipment delivery

- Impacts to agricultural production (if applicable)

- Land use impacts

- Impacts to aviation

- Setbacks, from both project property lines and sensitive receptors

Staff notes that the aforementioned list is not exclusive, and would encourage consideration of other factors that may not have been mentioned, in the EIS.

Staff notes that the Federal Register includes a reference to OPSB setbacks.  Section 4906.20(B)(2), Ohio Revised Code, discusses such applicable minimum setbacks.

Staff further recommends that the EIS consider the potential worst-case scenario for all of the variables within its scope of analysis so that the EIS results are robust and meaningful.  This would include, for instance, consideration of the tallest potential turbine models when evaluating shadow flicker, as well as the loudest turbine models under potential consideration when evaluating operational noise impacts.  If the impacts under the worst-case scenario are deemed reasonable after any appropriate avoidance and/or mitigation, then any deviation from those initial assumptions implicit in the worst-case scenario will only result in a beneficial reduction of potential impacts associated with the project.  Changes in this direction will be easier to incorporate during the review stage, as opposed to changes in which the impacts are subsequently expected to be greater than that assessed in the EIS.

Staff appreciates the opportunity to comment at this early stage in the process, and requests that OPSB Staff be added to the distribution list for the EIS.

Respectfully submitted,

Stuart M. Siegfried

Environmental Specialist

Ohio Power Siting Board Staff

180 E. Broad Street, 6th Floor

Columbus, Ohio 43215

(614) 466-7536

Stuart.Siegfried@puc.state.oh.us

# Footnotes

Ohio Rev. Code Ann. § 4906.13(A) (West 2010).

August 25, 2010 Federal Register, p. 52375

August 25, 2010 Federal Register, p. 52375