Ohio American Water Company

Franklin County District

Remedial Report for Unaccounted for Water

Actions/Progress Made in 2012 1st Quarter

- Continued to examine all reported “zero consumption” accounts for more than three (3) consecutive months for consumption.

  - Zero consumption meter readings have been verified that they are vacant, closed or no active accounts.

  - Consecutive estimate are down to less than one (1) for any single account.  Therefore water accounting by actual reading of meters appears correct.

- Obtained actual readings on all water service meters 3” and larger.

  - All 3” and larger meters have been read.

- Since all service areas’ water meters are read every month, meter readers have watched for potential water leaks while performing their meter reading routes.

- Repaired all reported company leaks within seven (7) days of verification of leak

Ohio American Water Company

Franklin County District

Remedial Report for Unaccounted for Water

Actions Plan for 2012 2nd Quarter

- Review Huber Ridge UFW to check for seasonal variations.

- Sound fire hydrants in the Huber Ridge service areas for non-surfacing leaks.

- Continue to have meter reads survey water lines along their meter routes each month for indications of leaks.